PART 1 GENERAL

1.1          RELATED DOCUMENTS

A.           Drawings and general provisions of the Contract, including General and Supplementary 			Conditions and Division 1 Specification Sections, apply to this Section.

1.2          SUMMARY

A.      	 Section Includes:

1. 	LEED Data: www.ecoscorecard.com

2.	Perforated and un-perforated metal ceiling panels

3. 	Acoustical backing.

4.	 Suspension Systems

5. 	Accessories; provide other necessary items including devices for attachment 				overhead construction, secondary members, splines, splices, connecting clips, wall 			connectors, wall angles, and other devices required for a complete installation.

6. 	Supplemental support framing: Provide fully engineered secondary framing as 				required to meet code, conforming to layout shown in drawings, to support 				direct-hung metal ceilings suspension system.

7. 	Coordinate layout and installation of items penetrating or being installed in 				ceiling systems with responsible trades.

B.	Related Sections / Work:

1.       Sections 05 40 00 – Cold-Formed metal Framing

2.       Sections 09 20 00 – Plaster and Gypsum Board

3.       Sections 09 50 00 – Acoustical Ceilings

4.       Sections 09 90 00 – Paintings and Coatings

5.       Division 23 – Heating, Ventilating and Air Conditioning

6.       Division 26 - Electrical

C.	Alternates (Substitutions):

1. 	Prior approval: unless otherwise provided for in the contract documents, 					proposed product substitutions may be submitted no later than 10 working days 				prior to the date established for receipt of bids.  Approval of a proposed 					substitution is contingent upon the Architect’s review of the proposal for 					acceptability. Approved products will be set forth by addenda.  If substitute 				products have not been approved by addenda, but are included in a bid, the 				specified products shall be provided without additional compensation.

2. 	Submittals which do not provide adequate data for the product evaluation will not 			be considered. The proposed substitution must meet the requirements for this 				section, including but not necessarily limited to the following: single source 				materials supplier (if specified in Section 1.5); panel design, size, composition, 				color and finish; suspension system component profiles and sizes; and compliance 			with the referenced standards

D.	This Section covers the general requirements only for Acoustical Metal Ceilings as 			shown on the drawings.  The supplying and installation of additional accessory feature 			and other items not specifically mentioned herein, but which are necessary to make a 			complete installation shall also be included or clarified accordingly.

E.	Qualification Data:

1.	Test Reports:  Certified reports from independent agency substantiating structural compliance to windloads and other governing requirements.

2.	Certificates:

a.	Data substantiating manufacturer and installer qualifications.

b.	Certified data attesting fire rated materials comply with specifications.

3.	Manufacturer’s Instructions:  Detailed installation instructions and maintenance data.

1.3          REFERENCES

A.             American Society for Testing and Materials (ASTM)

1.       E 84 – “Standard Test Method for Surface Burning Characteristics of Building 				Materials”

2.       E 488 – “Standard Test Methods for Strength of Anchors in Concrete and Masonry 				Elements”

3.       B 209 – “Standard Specification for Aluminum and Aluminum Alloy Sheet and 				Plate”

4.       C 423 – “Sound Absorption and Sound Absorption Coefficients by Reverberation 				Room Method”

5.       E 580 – “Standard Practice for Application of Ceiling Suspension Systems for 				Acoustical Tile and Lay-in Panels in Areas Requiring Moderate Seismic Restraint”

6.       C  635 – “Standard Specification for Metal Suspension Systems for Acoustical Tile 				and Lay-in Panel Ceilings”

7.       C 636 – “Recommended Practice for Installation of Metal Ceiling Suspensions 				Systems for Acoustical  and Lay-in Panels”

8.       A 641 – “Standard Specification for Zinc-Coated (Galvanized) Carbon Steel Wire”

9.       A 653 – “Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-				Iron Alloy Coated (Galvannealed) by the Hot-Dip process.

10.    E 1264 – Classification for Acoustical Ceiling Products”

11.    E 1477 – Standard Test Method for Luminous Reflectance factor of Acoustical

Materials by use of Integrating-Sphere Reflectometers”

12.    D 1044 – Practice for Abrasion Resistance

13.    D 1002 – Practice for Adhesion Resistance

B.            Applicable LEED Environmental Categories and Credits and performance requirements 			as indicated:

1.       Material and Resources (MR)

a.       MR Credit 4.1 & 4.2 – Recycled Content

b.       MR Credit 5.1 & 5.2 – Regional Materials

c.        MR Credit 7.0 – Certified Wood

2.       Indoor Environmental Quality (EQ)

a.       EQ Credit 4.1 – Low Emitting Materials, Adhesives & Sealants

b.       EQ Credit 4.1 – Low Emitting Materials, Paints

c.        EQ Credit 4.4 – Low Emitting Materials, Composite Wood & Agrifiber

3.       Innovation in Design (IC)

a.       IC Credit 1.1 – Enhanced Acoustical Performance

1.4          SUBMITTALS

A.	LEED - Product Data:  Manufacturers product data for each type of product specified in 			this section per ecoscorecard.com.

B.	Product Certification: Manufacturer’s certifications that products comply with specified 			requirements and governing codes including product data, laboratory test reports and 			research reports showing compliance with specified standards.

C.           Shop Drawings: Submit shop drawings for reflected ceiling plans (RCP’s), drawn to scale,

and indicating penetrations and ceiling mounted items.   Show the following details:

1.	Reflected Ceiling Plan(s):   Indicating metal ceiling layout, ceiling mounted items and penetration locations.

2.	Suspension System, Carrier and Component Layout.

3.	Details of system assembly and connections to building components.

D.	Samples for Verification: Full-size units (or as specified below) of each type of ceiling 			assembly indicated; in sets for each color, texture, and pattern specified, showing the 			full range of variations expected in these characteristics.  Submit samples for each type 			specified.

1.	 11-inch square, (acoustical) metal pan units.

2.	 11-inch long samples of each exposed molding or trim.

3.	 11-inch long samples of each suspension component.

1.5      	QUALITY ASSURANCE

A.	Manufacturer/Installer Qualifications:

1.	Provide metal ceiling system components produced by a single manufacturer with 			a minimum 5 years experience in actual production of specified products and with 			resources to provide consistent quality in appearance and physical properties, 				without delaying the work.

2.	Provide suspension system components produced by a single manufacturer to 				provide compatible components for a complete metal ceiling system installation.

3.	Perform installations using a firm with installers having no less than 3 years of 				successful experience on projects of similar size and requirements.

B.	Regulatory Requirements:

1.	Fire Rating Performance Characteristics:  Install system to provide a flame spread 				of 0 - 25, complying with certified testing to ASTM E 84.

2.	Structural Criteria:  Install and certify system to comply with structural and wind 				load requirements of governing codes.

3.	Installation Standard for Suspension System: Comply with ASTM C 636.

C.	Mock-Up:  Prior to beginning installation erect a mock-up section, where directed, using 			all system components.

D.	Pre-installation Conference:  Conduct a conference, prior to start of installation, to 			review system requirements, shop drawings, and all coordination needs.

1.6	DELIVERY, STORAGE AND HANDLING

A.	Deliver system components in manufacturer’s original unopened packages, clearly 			labeled.

B.	Store components in fully enclosed dry space.  Carefully place on skids, to damage from 			moisture and other construction activities.

C.	Handle components to prevent damage to surfaces and edges, and to prevent distortion 		and other physical damage.

1.7      	PROJECT CONDITIONS

A.	Begin system installations only after spaces are enclosed and weathertight, and after all wet work and overhead work have been completed.

B.	Prior to starting installations, allow materials to reach ambient room temperature and humidity intended to be maintained for occupancy.

1.8	WARRANTY

A.	Provide specified manufacturer’s warranty against defects in workmanship, 				discoloration, or other defect considered undesirable by the Architect or Employer.

B.	This warranty shall remain in effect for a minimum period of one (1) year from date of 			initial acceptance.

1.9	MAINTENANCE & EXTRA MATERIALS

A.	Maintenance Instructions: Provide manufacturers standard maintenance and cleaning 			instructions for finishes provided.

B.	Extra Materials: Furnish extra materials described below that match products installed, 			are packaged with protective covering for storage, and are identified with labels 			describing contents.  Only typical system components are included with attic stock.

1.       Acoustical Metal Ceiling Pan Units: Full-size units equal to 2 percent (2%) of 				amount installed.

2.       Ceiling Suspension System Components: Quantity of each grid and exposed 				component equal to 2 percent (2%) of amount installed.

PART 2 PRODUCTS

2.1      MANUFACTURER

A.	Provide “Luxalon” Linear metal ceiling system manufactured by Hunter Douglas Architectural Products, Inc., 5015 Oakbrook Parkway, Suite 100, Norcross, GA  30093, USA.  Ph. (800) 366-4327.

2.2      MATERIALS

A.	Linear panels for (interior) (exterior) installations:

B.	Panel Profile Type:  84R,  roll formed aluminum with round edges;  3 5/16 inch wide, 5/8 inch deep, (.020) (.025) (.032, exterior) inch thickness, with 11/16 inch reveal to form a 4 inch module and fabricated to snap-fit onto carriers with positive locking action.

- Panel length:  (Standard 12 feet) (minimum 3’ – maximum 16’) lengths.

- Perforation: (Non-perforated) (Perf 124, .025”) (Perf 140, .020”)

3.	Recessed Closure:  Roll-formed aluminum shaped to snap-fit between ceiling panels; black finish.

C. 	Panel Finish

1. 	Paint; color to be selected by architect

a.        Factory Applied Polyester

b.        Powder coat (.025)

D. 	LEED 2009 Reference Data:

1.  	Materials and Resources (MR)

a.        MR Credit 2 – Construction Waste Management

- painted aluminum panels are 100% recyclable.

b.        MR Credit 4 – Recycled Content

- 30% pre-consumer, 40% post-consumer

c.        MR Credit 5 – Regional Materials

- product manufactured at Hunter Douglas in Norcross, GA 30093

d.         MR Credit 7 – Certified Wood

- Luxalon Metal Ceilings, a division of Hunter Douglas Chain of Custody 				           Certificate Number is SCS-COC-003509

2. 	Indoor Environmental Quality (EQ)

a.        EQ Credit 4.1 – Low-Emitting Materials – Adhesives & Sealants

- product is Greenguard Air Quality Certified

- product is Greenguard for Children and Schools

b.        EQ Credit 4.2 – Low-Emitting Materials – Paints & Coatings

- product is Greenguard Air Quality Certified

- product is Greenguard for Children and Schools

3. 	Innovation in Design (IC)

- IC Credit 1.1 – Enhanced Acoustical Performance

2.3		METAL SUSPENSION SYSTEMS, GENERAL

A.	Carrier:  Type “V-7”, V shaped, .038 inch roll-formed aluminum section with hook

shaped tabs spaced to receive ceiling panels at 4 inch on center and 11/16 inch

apart.  Support holes spaced 4 inch on center.  Finish:  Factory applied black

enamel.

B.	Hanger Wire:  12 gage galvanized carbon steel hanger wire.

C.	Seismic / Wind Uplift Compression Struts:

2.4		CEILING  SYSTEM  ACCESSORY  MATERIALS

A.	Panel Splice:  Formed aluminum insert designed to snap-fit between ends of two

ceiling panels.

1.       Finish:  (Black)  (To match ceiling panels).

B.       	End Cap:  Formed aluminum for snap-fit.  Finish: (Black)  (To match ceiling

panels).

C.	Access Door:  (2 feet x 2 feet) (          feet x         feet) aluminum access frame with

hinges and retainer clip for downward acting access panel to plenum space.

D.	Acoustical Blankets:  (Minimum 1 inch thick 1 1/2 pcf fiberglass batts, black

finish with no surface printing)  (1 inch thick, 1 1/2 pcf fiberglass, encapsulated

in black polybag).

1.       NRC Rating: (.70 for non-perforated panel without filler strip)  (.90 for

perforated panel without filler strip).

E.	Air Distribution Devices:  Provide distribution devices that are independently

suspended, relocatable, adjustable from below finished ceiling, and capable of

being concealed behind (invisible to view) and fully integrated with ceiling

system so as to allow no interruption of ceiling components.

F.	Lighting Fixtures: Provide fixtures capable of being fully integrated with ceiling

system and requiring no interruption of ceiling components, that are

independently suspended, and as selected to conform to lighting criteria

specified in Division 16.

PART 3- EXECUTION

3.1      EXAMINATION

A.	Examine substrates and structural framing to which acoustical metal panels attach or 			abut, with Installer present, for compliance with requirements specified in this and 			other Sections that affect installation and anchorage, and other conditions affecting 			performance of metal panel ceilings.

B.            Proceed with installation only after unsatisfactory conditions have been corrected.

3.2      PREPARATION

A.	Coordination: Furnish layouts for cast-in-place anchors, clips, and other ceiling anchors 			whose installation is specified in other Sections.

B.            Measure each ceiling area and establish layout of acoustical metal pan units to balance 			border widths at opposite edges of each ceiling. Avoid using less-than-half-width units 			at borders, and comply with layout shown on reflected ceiling plans.

C.	Survey substrate for wall attachment to assure squareness and proper elevation for wall 		panel installation.

3.3      	INSTALLATION

A.           General: Install acoustical metal pan ceilings, per manufacturers shop drawings 				provided, per manufacturer's written instructions and to comply with publications 			referenced below.

1.       ClSCA "Ceiling Systems Handbook.

2.       Standard for Ceiling Suspension System Installations - ASTM C 636.

3.       Standard for Ceiling Suspension Systems Requiring Seismic Restraint - ASTM E 580

4.       IBC (International Building Code) standard for Seismic Zone for local area.

B.           Suspend ceiling hangers from building's approved structural substrates and as follows:

1.       Install hangers plumb and free from contact with insulation or other objects within 			ceiling plenum that are not part of supporting structure or of ceiling suspension 				system.

2.       Splay hangers only where required to miss obstructions; offset resulting horizontal 			forces by bracing, counter-splaying, or other equally effective means.

3.       Where width of ducts and other construction within ceiling plenum produce 				hanger spacings that interfere with location of hangers at spacing required to 				support standard suspension system members, install supplemental suspension 				members and hangers in form of trapezes or equivalent devices. Size 					supplemental suspension members and hangers to support ceiling loads within 				performance limits established by referenced standards and publications.

4.       Where used secure wire hangers to ceiling suspension members and to supports 				above with a minimum of three tight turns. Connect hangers directly either to 				structures or to inserts, eye screws, or other devices that are secure; that are 				appropriate for substrate; and that will not deteriorate or otherwise fail due to 				age, corrosion, or elevated temperatures.

5.       Space hangers not more than 48 inches on center, along each member supported 				directly from hangers, unless otherwise indicated; and provide hangers not more 				than 8 inches from ends of each member. Supply supporting calculations from 				licensed Structural Engineer verifying hanger spacing meets all requirements, 				when spacing exceed those recommended.

6.       Fine level grid to 1/8 inch in 10 feet from specified elevation(s), square and true.

7.       Adjust suspension system runners so they are square (within .5 degree from 90 				degrees) and securely interlocked with one another. Remove and replace dented, 				bent, or kinked members.

C.            Secure bracing wires to ceiling suspension members and to supports acceptable to 			Architect / Engineer and or inspector. Suspend bracing from building's structural 			members and / or structural deck, as required for hangers, without attaching to 				permanent metal forms, steel deck, or steel deck tabs(unless directed otherwise).

D.	Install edge moldings and trim of type indicated at perimeter of acoustical ceiling area 			and where necessary to conceal edges of acoustical metal pan. Method of edge trim 			attachment and design of edge trims to be approved by Architect.

1.       Screw attach moldings to substrate at intervals not more than 18” O.C. and not 				more than 6” from ends, leveling with ceding suspension system to a tolerance of 				1/8” in 10’.  Miter corners accurately and connect securely.

2.       Do not use exposed fasteners, including pop rivets, on moldings and trim 					without prior written approval. Or unless detailed otherwise.

F.	Scribe and cut acoustical metal panel units for accurate fit at penetrations by, other 			work through ceilings. Stiffen edges of cut units as required to eliminate evidence of 			buckling or variations in flatness exceeding referenced standards for stretcher-leveled 			metal sheet.

G.	Install acoustical metal panel units in coordination with suspension system.

1.       Align joints in adjacent courses to form uniform, straight joints parallel to room 				axis in both directions, unless otherwise indicated.  Install directionally patterned 				or textured panels in directions indicated on approved shop drawings.  Panel-				joints shall flow smoothly and in a straight line within 1/8” in 10’. Intersections 				shall be continuous.

2.       Fit adjoining units to form flush, tight joints. Scribe and cut units for accurate fit at 				borders and around construction penetrating ceiling.

3.       Remove protective film from panels only when space is completely clean and free 				of airborne particles. Use white cotton gloves for final installation of panels into 				grid system.

3.4		ADJUST AND CLEAN

A.	Adjust components to provide uniform tolerances.

B.	Replace all ceiling panels that are scratched, dented or otherwise damaged.

C.	Clean exposed surfaces with non-solvent, non-abrasive commercial type cleaner.

End of section