# SECTION 12492 – MANUAL ROLLER SHADES

# PART 1 – GENERAL

  - SUMMARY

- Section includes

  - Manually operated Roller Shades

- Related work includes the following:

  - Section 06100: Rough Carpentry

  - Section 08520: Aluminum Windows

  - REFERENCES

- National Fire Protection Association (NFPA) 701

B.	Department of Transportation Motor Vehicle Safety Standard 302 Flammability of Interior Materials

C.	California Administrative Code Title 19

- Federal Standard 191 Method 5903 (used by Port Authority of New York and New Jersey for drapery, curtain, and upholstery material)

- Boston Fire Department Teat BFD IX-1

- New York State Uniform Fire Prevention and Building Code

  - SUBMITTALS

- Subject under provisions of Section 01330 – Submittal Procedures

- Product Data: Manufacturer’s data sheets shall be submitted for each product specified, including:,

  - Preparation instructions and recommendations

  - Finishes, material descriptions, dimensions of individual components

  - Construction and installation instructions

  - Manufacturers recommendations for maintenance and cleaning

- Drawings and Diagrams: Product details, installation details, working and assembly drawings shall be supplied as requested.

- Sample: Responsible contracting officer or agent shall supply one sample shade of each type specified in this contract for approval. Supplied units shall be furnished complete with all required components, mounting and associated hardware, instructions and warranty.

  - QUALITY ASSURANCE

- Supplier: Manufacturer, subsidiary or licensed agent shall be approved to supply the products specified, and to honor any claims against product presented in accordance with warranty.

- Installer: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer shall be responsible for an acceptable installation.

- Uniformity: Provide Manual Roller Shades of only one manufacturer for entire project.

D.	Mock up: Provide (1) mock-up shade for each roller shade type/assembly specified.

1.5 	DELIVERY, STORAGE AND HANDLING

- Product shall be delivered to site in manufacturer’s original packaging.

- Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

1.6	JOB CONDITIONS

- Prior to shade installation, building shall be enclosed.

- Interior temperature shall be maintained between 60° F. and 90° F. during and after installation; relative humidity shall not exceed 80%. Wet work shall be complete and dry.

  - WARRANTY

- Lifetime Limited Warranty. Fabrics warranted for 5 years. Specific product warranties available from manufacturer or its authorized agent.

PART 2 – PRODUCTS

2.01	ACCEPTABLE MANUFACTURER

- Hunter Douglas Contract/ 13915 Danielson St., Ste.100/ Poway, CA 92064/ Phone: 800-727-8953 Fax: 800-205-9819/ Website: www.hunterdouglascontract.com, or architect approved equivalent. Contact the following for project assistance and dealer referral @ 800-964-2580: (Mideast/Midwest) Keith Burgess ext. #827311, (Southern/Central) Christopher Hagen ext. #827312, (Western/Mountain/Upper Midwest) David Cover ext. #827313, (Northeast) Patrick LeClair ext. #827314, (Southwest) Matthew Craven ext. #827317, (Southern Atlantic) Carol Addison ext. #827320.

- Request for substitutions must be approved by architect minimum of 30 days prior to close of bid.

2.02	MANUAL ROLLER SHADES

A.	PRODUCT: Hunter Douglas Contract “RB 500 Manual Roller Shades”

B.	MATERIALS:

  - FABRICS: Inherently anti-static, flame retardant, fade and stain resistant, light filtering, room darkening, & blackout fabrics providing 0% - 14% openness factors. Fabric weights to range between 6.00 oz/sq.yd. – 20.70 oz/sq.yd., containing fiberglass, PVC, polyester, acrylic, vinyl laminates, cotton, & vinyl coatings. Finish selected by architect from manufacturer’s available contract colors.

  - CONTROL SYSTEMS:

A. CLUTCH OPERATED: Engineered heavy duty chain drive pulley operating system consisting of metal clutch housing and locking plug containing minimum 6 ribs and inserted at minimum of 2-1/4” into roller tube. Lift torque enhancement provided by Counter Balance System with integrated spring support module. Utilization of adjustment-free continuous qualified T304 stainless steel ball chain with 110 lbs breaking strength for precise control, smooth operation and ensuring a uniform look. Chain tensioner to be compliant with WCMA safety standard A100.1-2010 and must prevent the clutch system from moving the roller shade through lowering and raising if not properly installed as specified in ANSI Standard Section 6.5.2. Components will be maintenance free from adjustments or lubrication for trouble-free operation.

B. CRANK OPERATED: Gear box assembly made from die cast aluminum and steel construction with steel crank insert. Permanent (or detachable) steel handle with flexible universal joints for easy turning force.

  - DUAL ROLLER SHADES: Universal mount steel brackets with 2 separate solar and room darkening blackout roller shades operating independently of each other.

  - ROLLER TUBE: Circular-shaped aluminum tube extruded from alloy and temper 6063 T-6. 2”outside diameter extruded tube to have a .063” wall thickness (2.5” outside diameter to have a .079” wall thickness). Heavily reinforced with minimum six internal ribs providing additional tensile strength and allows for secure placement of clutch & end plug.

5.	HEAVY DUTY TUBE BEARING PLUG: Die cast metal and reinforced idler assembly containing spring loaded end plug with positive locking wheel allows for up to 7/8” adjustment and provides for a secure installation and removal of shade. Locking tube bearing plug contains minimum 6 ribs and inserted a minimum of 2-3/8” into roller tube.

  - BOTTOM BAR: Extruded aluminum weight in a Sealed Pocket Hem Bar, or RB Bottom Bar for fabrics that are not seamable. Bottom bar is for tracking adjustments and provides uniform look.

  - MOUNTING HARDWARE: Manufacturer’s standard heavy duty bracket constructed of hardened 1/8” thick steel to support full weight of shade with  bracket & screw hole covers to provide uniform look. Integrated leveling device for enhanced level adjustment of overall shade. Locking mechanism on bracket adapter provides for a secure installation and removal of the shade.

  - FASCIA: L shape removable aluminum extrusion valance that attaches to brackets and conceals roller shade.

  - ROLLER SHADE POCKET: Extruded aluminum alloy U shape housing for recessed mounting in acoustical tile or drywall ceilings. 5.25” (or 9”) in diameter with aluminum closure mount.

  - BLOCKOUT SYSTEM: Extruded aluminum side channel with concealed mounting brackets. Bottom bar with nylon wool pile to prevent light leakage.

  - ADDITIONAL AVAILABLE OPTIONS: RB500 Bottom Bar, Reverse Roll, Detachable Spline, Internal Auto Stop Mechanism, Coupled and Banded

2.03	FABRICATION

A. 	Shade measurements shall be accurate to within + 1/8” or as recommended in writing by manufacturer.

2.04 	FABRICS

A. 	FABRIC selection from the following: (0% Openness) Avila Twilight, Edessa Twilight, Geneva Twilight, Flocke, Morocco, Pima, Sheerweave 7000, Sheerweave 7100, Sheerweave 7300 (1% Openness) GlacierScreen HD2001, GreenScreen Revive 1%, E Screen 7501,Vizela, Sheerweave 7350, Sheerweave 2701, Sheerweave 4800 (3% Openness) GlacierScreen HD1003, GlacierScreen HD2003, GreenScreen Eco, GreenScreen Revive 3%, T Screen, E Screen 7503, E Screen 7703 KoolBlack, M Screen 8503, T Screen, Sheerweave 2410, Sheerweave 2410 Performance +, Infinity2, Sheerweave 2703, Sheerweave 4400, Sheerweave 4600, Sheerweave 4650, (4% Openness) Star 2115 (5% Openness) GlacierScreen HD1005, E Screen 7505, E Screen 7705 KoolBlack, Cortina, Satine, M Screen 8505, M Screen Deco, SilverScreen, Sheerweave 2000, Sheerweave 2390, Sheerweave 2390 Performance +, Sheerweave 2705, Sheerweave 4000, Sheerweave 4500, Sheerweave 4550, Sheerweave 4700, Sheerweave 5000, (7% Openness) Siena (10% Openness) GlacierScreen HD1010, E Screen 7510, Vienne, New Orleans, Sheerweave 2100, Sheerweave 2360, Sheerweave 2710, Sheerweave 4100 (12% Openness) Natte (14% Openness) A Screen, Sheerweave 3000.

PART 3 - EXECUTION

3.01 	INSPECTION:

A.	SUBCONTRACTOR shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

B.	OTHER INTERACTING TRADES shall receive drawings of shade systems, dimensions, assembly and installation methods from subcontractor upon request.

3.02	INSTALLATION:

A.	INSTALLATION shall comply with manufacturer’s specifications, standards and procedures as detailed on contract drawings.

B.	ADEQUATE CLEARANCE shall be provided to permit unencumbered operation of shade and hardware.

C.	CLEAN finish installation of dirt and finger marks. Leave work area clean and free of debris.

3.03	DEMONSTRATION:

A. 	Demonstrate operation method and instruct owner’s personnel in the proper operation and maintenance of the roller shades.

3.04	SCHEDULE:

A.	EXTERIOR WINDOWS:

B.	INTERIOR RELIGHTS:

END OF SECTION 12492